## Slide 1
Overview, Features and Changes

## Slide 2: OUTLINE
What’s New
  New EZ Model
  Field Gas Conversion
  EZ Start Plus Bluetooth App
  Built in Display Window
  Front Cover Latches
Model Specifications
Installation
  Venting
  Gas
  Condensate
  Unit Settings
  Basic Maintenance

## Slide 3: 10+ YEARS OF EZTR INNOVATION
It all started in 2014 with the EZTR40 package, offering installers a time saving and EZ way to replace a tank with a tankless utilizing top mounted water connections. In 2017 the Pre-Mix EZ and EZTR models were introduced offering higher efficiency and capacities. In 2020 the EZ/EZTR Pre-Mix lineup was expanded to include the NRCR along with new features like Steady BTU. Now, the latest EZ and EZTR models offer even higher efficiency and more features including a new EZ71 model!
2014
2017
2020
2024

## Slide 4: WHAT’S NEW?

## Slide 5: WHAT’S NEW
.98 UEF for all models
  Highest UEF for complete BTU range in the industry
New EZ Model
  160kbtu EZ71 Model Added
Field Gas Conversion
  Default setup for NG, conversion included to change to LP without the need to order a gas conversion kit.
EZ Start Plus Bluetooth App
  Physical dipswitches are gone! Unit setup is done entirely through Bluetooth app.
Built in Display Window
  Remote control is optional. Maintenance Monitors and Unit Settings can be accessed through the Display Window.

## Slide 6: NEW LEVEL OF EFFICIENCY
The new EZ Series Pro and the entire new Pre-Mix line up all achieve a .98 UEF making them among the most efficient tankless models on the market.
2014
2017
2020
2024
.87 UEF
.96 UEF
.96 UEF
.98 UEF

## Slide 7: NEW EZ71 MODEL
With the addition of the EZ71, there is now an EZ unit for those smaller applications where a larger unit doesn’t make much sense.
The EZ71 will be available as an individual unit and not part of an EZTR package, however you may still use the flex vent conversion and flex vent kit like any other EZ unit.

## Slide 8: FIELD GAS CONVERSION
All EZ Series Pro and future Pre-Mix models are ready to be used with NG. If the jobsite has LP, a simple field gas conversion can be performed without the need to purchase any additional parts. Conversion is EZ and can be done in about 5 minutes.
Conversion Kit taped to top of unit
Contents of LP Conversion Kit

## Slide 9: FIELD GAS CONVERSION
Step 1
Remove screw
Step 2
Remove the c-clip
Step 3
Carefully remove gas fitting
Step 4
Remove 2 screws securing venturi fitting

## Slide 10: FIELD GAS CONVERSION
Step 5
Remove NG orifice
Step 6
Step 7
Insert gas fitting, secure c-clip and screw
Step 8
Secure venturi fitting
Insert LP orifice
(make sure o-ring and gasket aren’t lost or damaged)
O-RING
GASKET

## Slide 11: FIELD GAS CONVERSION
Step 9
Plug in LP conversion connector
Step 10: Changing gas type to LP with EZ Start Plus App
Open EZ Start Plus App and select Contractor
Enter Passcode and tap “NEXT”
Make sure Bluetooth is ON
Select Unit then tap OK
*Built in display can also be used to convert gas type, see gas conversion directions included with unit

## Slide 12: FIELD GAS CONVERSION
Step 10 (continued): Changing gas type to LP with EZ Start Plus App
Tap “Unit Setting”
Tap Change Setting, Tap LP then tap “DONE”
Tap “Convert Gas Type”
After a few seconds it should show complete
Register Warranty or skip

## Slide 13: FIELD GAS CONVERSION
MAKE SURE TO FILL OUT AND ATTATCH GAS CONVERSION STICKER TO UNIT

## Slide 14: EZ START PLUS APP
Initial unit setup, temperature adjustment and maintenance can all be handled through the new EZ Start Plus Bluetooth App!
The App will walk you through setting up the unit upon completing installation and provides an easy way to register the unit for your customers.
Error Code History can be accessed and will link you directly to help articles related to any error codes stored.

## Slide 15: BUILT IN DISPLAY WINDOW
Displays temperature setting, service reminders and error codes. Also allows you to view maintenance monitors, error code history and change installation settings. The new display window makes the remote control a truly optional item.

## Slide 16: NEW LATCHED FRONT COVER
Easier access when performing preventative maintenance, service or operating the built in display window. Remove 2 screws at the bottom of the front cover and the latches hold the cover in place until you’re ready to remove it.

## Slide 17: MODEL SPECIFICATIONS

## Slide 18: EZ SERIES SPECIFICATIONS
NEW

## Slide 19: EZ PERFORMANCE
Need more flow? Quick Connect two identical EZ units and double the flow!

## Slide 20: INSTALLATION

## Slide 21: PRE-INSTALLATION CHECKS
Verify the following before installation and read the manual:
Check the gas:
EZ71 Max btu is 160k
EZ98 Max btu is 180k.
EZ111 Max btu is 199k.
Ensure the existing gas system can support that demand + other existing gas demands.
Check the power:
EZ Series and all Noritz units operate on 120 VAC at 60Hz.
Check the vent:
EZ Series uses plastic venting (PVC, CPVC and PP).
Existing venting will likely have to be replaced unless you are replacing a similar type unit.
Exhaust leaks into the home may lead to injury or death. Do not take shortcuts here.

## Slide 22: EZ UNIT MOUNTING
Mount bracket, hang heater and shift side to side for precise alignment, secure heater.

## Slide 23: EZ VENTING OPTIONS
As with previous models, you have the ability to install the unit indoors or outdoors with a variety of venting options.
Indoor DV
Max Vent Lengths DV or SV:
2”: 75 Feet, 3”: 150 Feet, 4”: 65 Feet
Indoor SV
Indoor FSV
Outdoor
Indoor NRK

## Slide 24: EZ NO ROOF KIT
Have a straight run of b-vent? The No Roof Kit makes it even EZ’er to replace a tank!
Features:
Faster Installation without roof access
Up to 8.5’ venting available
Available for 3” and 4” round b-vent
Less material waste
The No Roof Kit comes with all accessories needed for installation*:
*PVC Parts must be field supplied
Diffuser Kit
SV Conversion Kit
Polypropylene Kit
Item #: NRK-1

## Slide 25: EZ 2 INCH FLEX VENT
Use existing 3” or 4” round b-vent.
2 additional parts numbers required*:
⚫ EZ2-CK or EZ2-CK-1: Conversion kit to adapt unit to accept flex vent.
⚫ EZ2FVK-1 (25 ft.) or EZ2FVK-2 (35 ft.): Select either 25 ft. or 35 ft. depending on length of existing b-vent.
NOTE: Flexible vent can be shortened but you cannot join 2 pieces of flexible vent to extend the length.
*NOT Required if an EZTR package is purchased.

## Slide 26: INSTALLATION CLEARANCES
Verify the following before installation and read the manual
Select a proper installation location:
Maintain minimum required clearances and if possible, recommended clearances.
Required
Recommended
Cooking Equipment

## Slide 27: INSTALLATION CLEARANCES
Verify the following before installation and read the manual
Select a proper installation location:
Maintain minimum required clearances and if possible, recommended clearances.
Required
Recommended
Cooking Equipment
Recommended clearances are not only there to provide enough space for inspection, maintenance and repair but also to make sure the homeowner has quick and unimpeded access to gas and water shut off in the unlikely event of an emergency.

## Slide 28: EZ ½” GAS LINE CONDITIONS
½” Gas line is still an option with the new EZ Series Pro assuming an 8” WC or higher initial starting pressure. As always, make sure to follow the gas sizing tables in the installation manual.

## Slide 29: EZ GAS LINE CONDITIONS
General gas guidelines.
Test inlet pressure after installation:
Low demand (1 or 2 fixtures)
Moderate demand (3 or 4 fixtures)
High demand (5+ fixtures)
Worst case scenario, 5+ fixtures + all other gas appliances.

## Slide 30: EZ GAS LINE CONDITIONS
An improperly sized gas line generally results in one or more of the following issues:
Ignition Failure (Error Code 11)
Flame Loss (Error Code 12)
Abnormal Combustion (Error Code 10 or 90)
Fluctuating water temperatures
Abnormal noises
Other items in the gas supply system that could cause problems:
Meter size
Water/debris in gas line
Earthquake safety shutoff valve (California specific)

## Slide 31: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Horizontal

## Slide 32: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Horizontal

## Slide 33: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Horizontal
(Option 1)

## Slide 34: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Horizontal
(Option 2)

## Slide 35: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Horizontal
(Option 3)

## Slide 36: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Horizontal
(Concentric)

## Slide 37: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Vertical

## Slide 38: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Direct Vent Vertical
(Concentric)

## Slide 39: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Single Vent
Horizontal
Vertical

## Slide 40: EZ VENTING GUIDELINES
Wide variety of venting options for an EZ install.
Outdoor
Flexible Vent

## Slide 41: EZ COMMON VENT
EZ installation of 2 units.

## Slide 42: CONDENSATE DRAIN LINE
Guidelines for routing the condensate drain line.

## Slide 43: PROGRAMMING THE UNIT
The EZ Series Pro no longer has physical dipswitches on the circuit board. All programming of the unit is done with the new EZ Start Plus App or the built in display window.
Directions can be found in the manual

## Slide 44: EZ START PLUS APP
Open EZ Start Plus App and select Contractor
Enter Passcode and tap “NEXT”
Make sure Bluetooth is ON
Select Unit then tap OK

## Slide 45: EZ START PLUS APP
Select Options Based on Installation then tap NEXT
Tap “Unit Setting”
Register Warranty or skip
Tap “Unit Setting”

## Slide 46: EZ START PLUS APP
Upon completion, email app will open to allow emailing the installation settings to Noritz. This is not required, but very helpful for Customer Care.
Please fill out these items if you opt in to send.
Review your selections then tap DONE
App programs unit
Tap OK when complete

## Slide 47: BASIC MAINTENANCE
Keep the unit performing to its potential

## Slide 48: WATER QUALITY
Water Quality Guidelines in the Installation Manual should always be followed.

## Slide 49: POOR WATER QUALITY ISSUES
Here are some issues related to Hard Water or Poor Water Quality:
Scale Buildup
Overheated Water Temperature
Error Codes: 14, 16, 20, 65
Clogged Inlet Filter Screen

## Slide 50: DESCALING/FLUSHING
So, what do you need to perform a proper descale?

## Slide 51: DESCALING/FLUSHING
The flush connector is gone and descale mode is started with the EZ Start Plus App or the built in display.
Directions can be found in the manual

## Slide 52: HELPFUL LINKS
SUPPORT.NORITZ.COM
NORITZ.COM/TECHTIPS
HELP.NORITZ.COM
TRAINING.NORITZ.COM
YOUTUBE.COM/NORITZAMERICA
Customer Care: 866-766-7489

## Slide 53: THANK YOU