## Slide 1
The Original Tankless Water Heater Manufacturer and World Leader in Tankless Technology since 1951

## Slide 2
NCC300OD & NCC300DV
NC380-SV-ASME
NCC199CDV
Hybrid Hot System
CMK & CRK Manifold Systems
CR61 Systems
TTS – S and SWH Series
TTS – TWST Series
Sizing and FIOP (Factory Installed Options)
INTRODUCTION

## Slide 3
Indoor Model: NCC300DV (4” PVC, CPVC, PP and 5” SS w/ adapters)
Outdoor Model: NCC300OD (no vent cap required)
BTU Range: 15,000 – 300,000 BTUh
Flow Range: 0.5 – 13.2 gpm
Temperature Range: 100 F – 185 F
Thermal Efficiency: 97%
Turndown Ratio: 20:1
Multi System: up to 24 units (up to 7.2 million BTUh)
Warranty: 5 yr HEX, 5 yr parts, 1 yr labor
HEX: K type copper (primary) SS (secondary)
Sales only in CA, MN & WI
NCC300 SERIES

## Slide 4
Flow Rates and Pressure Loss
NCC300 SERIES

## Slide 5
Non-Condensing - Indoor/Outdoor Installations
Indoor – 5” Cat III Stainless Steel Venting
Outdoor – Vent Cap Required (VC-132)
BTU Range: 22,500 – 380,000 BTUh
Flow Range: 0.7 – 13.2 gpm
Temperature Range: 100 F – 180 F
Thermal Efficiency: 80%
Multi System: up to 24 units (up to 9.1 million BTUh)
Warranty: 5 yr HEX, 5 yr parts, 1 yr labor
HEX: K type copper
NC380-SV-ASME

## Slide 6
Flow Rates and Pressure Loss
NC380-SV-ASME

## Slide 7
Indoor/Outdoor Model (Versatile Venting)
Indoor: 2”- 75’, 3”- 150’ or 4”- 65’ PVC/CPVC/PP
Outdoor: Vent Cap required (VC-6-1)
BTU Range: 12,800 – 199,900 BTUh
Flow Range: 0.4 – 11.1 gpm
Temperature Range: 100 F – 185 F
Thermal Efficiency: 98% (UEF 0.98)
Turndown Ratio: 16:1
Multi System: up to 24 units (up to 4.8 million BTUh)
Warranty: 10 yr HEX, 5 yr parts, 1 yr labor
HEX: Stainless Steel for both Primary and Secondary
NCC199CDV PRO SERIES

## Slide 8
NCC199CDV PRO ADD’L FEATURES
Bluetooth Connectivity: EZ Start Plus App
Wi-Fi Capable
Operation Panel
Service Reminder
Field Convertible: LP parts included in box
Built in non-return valve
Common Vent up to 12 units
High Altitude Approved up to 10,200 ft
Scale Detection
Pre-Mix Burner w/ Negative Pressure Gas Valve
Quick Connect Capable up to 8 units

## Slide 9
Flow Rates and Pressure Loss
NCC199CDV PRO SERIES

## Slide 10
NCC199CDV PRO MULTI UNIT SYSTEMS
Quick Connect Cord (QC-2)
System Controller (SC(U)-##M)
Superior commercial unit linking made easy
Up to 24 units (6, 12 & 24)
Stages, rotates, load balances
Settings types:
Standard, Recirculation, Storage
Aquastat & Timer
Fan Control (External)
Up to 8 units
Stages, rotates, load balances

## Slide 11
NCC199CDV PRO MULTI UNIT SYSTEMS
If using QC Cords: purchase one less than the number of units
  Example: 6 units you will need qty 5 of the QC-2
If using 6-unit system controller, need to purchase:
1x SC-401-6M System Controller
1x of the RC-9018M Remote
Qty equal to the number of units of the RC-CORD10 or RC-CORD26 (10 ft or 26 ft Remote Cords)
Example 4 units: you will need 1 System Controller, 1 Remote, 4 Remote Cords
If using 12 or 24 unit system controller, need to purchase:
1x SCU-401-12M (or -24M) System Controller
1x RC-9018M (Remote)
Qty +1 the number of units of the RC-CORD10 or RC-CORD26 Remote Cords
  Example 10 units: you will need 1 System Controller, 1 Remote, 11 Remote Cords

## Slide 12
Units must be connected in series using QC cords (QC-2)
QC cords are not included in box (purchased separately)
For all sub units, the QC cord runs from Qcc-1 (white) to Qcc-2 (red) on the subsequent units
Leader
Follower
Qcc-2
UNUSED
Qcc-1
Qcc-1
UNUSED
※Qcc-1 OPEN
“Last Follower”
Optional
RC-9018M
Image of QC connectors
Follower
Follower
Follower
Follower
Qcc-2
Qcc-1
Qcc-2
Qcc-1
Qcc-2
Qcc-1
Qcc-2
Qcc-1
Qcc-2
NCC199CDV PRO QUICK CONNECT

## Slide 13
NCC199CDV PRO MULTI UNIT SYSTEMS
1x RC-9018M
Commercial Remote
Remote Cords: Total qty of units
RC-CORD10 (10ft Cord)
RC-CORD26 (26ft Cord)
Example: 4 Units = 4 Remote Cords, 1 System Controller and 1 Commercial Remote.
1x SC-401-6M
System Controller

## Slide 14
NCC199CDV PRO MULTI UNIT SYSTEMS
1x SCU-401-12M (or 24M) System Controller
1x RC-9018M
Commercial Remote
Remote Cords:
Total qty of units +1
RC-CORD10 (10ft Cord)
RC-CORD26 (26ft Cord)
Example: 10 Units = 11 Remote Cords, 1 System Controller and 1 Commercial Remote.

## Slide 15
VENT MATERIALS
Fill the condensate container by pouring approx. 10
oz. (280 mL) of water into the exhaust flue on the
top of the water heater as illustrated below.
If the vent pipe has already been installed:
After installing the condensate drain pipe, make
sure that the area around the water heater is well
ventilated. Open a window or a door if necessary.
Then operate the water heater and check that
condensate comes out of the condensate drain
pipe.
(During normal use of the water heater, condensate
will usually begin to discharge from the condensate
drain pipe within 15 minutes of use, but it may take
longer depending on the season and/or installation
site conditions.)
This is a Category IV appliance.
Only vent materials approved for use with Category IV appliances may be used.
Under normal conditions, this water heater will not produce an exhaust flue Temperature greater than 149°F (65°C) and schedule 40 PVC pipe may be used as the vent material. If the water heater set temperature is 160°F (70°C) or higher and there is a return line to the water heater from either a recirculation pump or a combination space heating system, schedule 40/80 CPVC, polypropylene or stainless steel must be used.

## Slide 16
NCC199CDV PRO VENT VERSATILITY
Direct Vent
Single Vent
Common Single Vent
Common Direct Vent
Outdoor

## Slide 17
COMMON VENTING
Up to 12 Noritz Water Heaters can share the same venting system. This means significantly reduced penetrations through the wall or roof resulting in less labor and a cleaner finished look. The use of a larger vent diameter system allows for longer vent runs for larger and taller building – up to 200 ft. of equivalent length.
OFFERS A CLEAN, LABOR SAVING INSTALL WHILE ENSURING THE UTMOST IN SAFETY AND PERFORMANCE
  Tested with safety in mind – each water heater has a built-in non-return valve to prevent flue gas from entering idle units.
  Reduces wall or ceiling penetrations.
  Utilizes either ULCS-636 approved Polypropylene (PP) venting (capable of handling temperatures up to 230° F) or Schedule 40/80 PVC.

## Slide 18
COMMON VENT OPTIONS
Ultimate Flexibility
Figuring out where to safely and efficiently route the exhaust system is one of the biggest hurdles for any HVAC system designer.
Noritz Common Venting offers designers the most flexibility to decide how to safely and efficiently route the vent. For room air installations, the combustion air can be drawn from the room environment, further reducing the installation complexity, by requiring only a single penetration for the exhaust.

## Slide 19
COMMON VENT LENGTHS
When counting the number of elbows, DO NOT include the termination, see next slide
* The Btu/h input of the unit will be reduced by up to 9%
NOTE: The sizing method shown in this table is provided for the convenience of the installer. Maximum acceptable vent system static pressure drop is 0.6” WC.

## Slide 20
COMMON VENT LENGTHS
Total Equivalent Length
= 35 ft + 2 x 5 ft (3” Elbow)
= 45 ft < 65 ft (Refer to table)
3” Vent System is Suitable
Total Equivalent Length
= 60 ft + 4 x 12 ft (4” Elbow) = 108 ft > 65 ft (Refer to table)
4” Vent System is NOT Suitable
= 60 ft + 4 x 18 ft (6” Elbow) = 132 ft < 200 ft (Refer to table)
6” Vent System is Suitable

## Slide 21
COMMON VENT EXAMPLES

## Slide 22
COMMON VENT EXAMPLES
6 Units in-line PVC DV

## Slide 23
Does not need an external Non-Return Valve. Built in one is CSA certified and satisfies their requirements (less cost to common vent).
External Non-Return Valve Not Required because
of integrated Internal Back Flow Damper for Common Venting.
This System w/o NRV is certified and satisfies CSA safety guideline.
BUILT-IN BACK FLOW PREVENTER
Notes: No longer requires an external Non-Return Valve which could add an additional $300 premium per heater to common vent. The Non-Return Valve is now integrated into the unit between the fan motor assembly and combustion box satisfying CSA safety guidelines.

## Slide 25
THE BEST OF TANK AND TANKLESS
With an endless supply of hot water, lower pressure drop, and no limitation of hot water flow rate, the Hybrid Hot Series by Noritz combines features of both technologies to provide the most reliable hot water delivery system to date for commercial applications.
CONTINUOUS HOT WATER DELIVERY
If your tank suddenly runs out of hot water, no need to worry. The Hybrid Hot Series by Noritz can continue to provide hot water using the paired NCC199CDV tankless even after your stored supply is depleted*. (*Hot water capabilities are limited)
FASTER HOT WATER RECOVERY
The Hybrid Hot offers the best BTU possible at the quickest rate, providing businesses with energy savings and more.
CEMENT LINING
With no anode rod and a greater warranty than other tanks on the market, our tank also features cement lining for superior corrosion resistance.
The Hybrid Hot Series by Noritz brings together the storage of a standard tank and the power and efficiency of a tankless to take on any commercial hot water demand.
Combined to meet the hot water requirements of businesses, the Hybrid Hot Series by Noritz utilizes the latest in tankless and tank storage technologies to create a powerful and reliable solution for businessowners. The Hybrid Hot also offers common venting for multiple units to ensure endless hot water is always available.
Assembled in the USA
NHH199100

## Slide 26
NHH199100

## Slide 27
The NCC199CDV on the Hybrid Hot Unit comes programmed from the factory to function like a tankless and storage system without the system controller.
NHH199100

## Slide 28
A Standard Efficiency Commercial Gas water Heater can reach temperatures over 500ºF at the burner chamber. The constant expansion and contraction of the steel tank and heat related stresses to the tank can, over time shorten its life (Stress Crack Corrosion).
Add in the accumulation of scale build up in the bottom of the tank (covering the burner) acting as an insulated layer. Causing the heater to fire longer each time the tank needs to be regenerated.
These main two factors add to shorter tank life. The hotter the outlet water needs to be, the more effect it will have on the tank.
AO Smith Cyclone
THERMAL CYCLING & HEAT STRESS

## Slide 29
Our Hybrid Hot by Noritz reduces the amount of heat stress and thermal wear to the tank by up to 2/3 of commercial tank heaters. The Hybrid Hot storage tank will never see temperatures above 185ºF.
Also, with no burner under the tank, expansion and contraction of the tank will be held to a minimum.
Our concrete lined tank adds another layer of protection.
THERMAL CYCLING & HEAT STRESS

## Slide 30
Hydrastone Lining
A seamless ½” thick lining is impervious to adverse water conditions and is proven to be the most effective method of preventing tank failure due to corrosion. Hydrastone lining absorbs and traps water, which then loses its oxygen and becomes inert, thus preventing tank corrosion.
Premium Insulation
2” thick polyurethane foam combined with heat-retaining Hydrastone lining allows less than 0.3ºF heat loss per hour.
0.005” Glass lined storage tanks require an anode rod to attract the corrosive minerals that attack the water heater
CEMENT LINED VS. GLASS LINED

## Slide 31
Recirc Port
Gas Port
Condensate Drain
Thermistor
(on tank surface)
Drain Port &
Wye Strainer
Tank Outlet Port
T&P Relief Valve
Hot Water Line
Pump
Cold Water Line
Tank Inlet Port

## Slide 32
Blend water to Tankless
Inlet Cold to the tank
Hot out to storage
Hot out to System
Return Loop
Check Valve
Recirc Pump
System Pump
1 ½” NPT Hot Outlet
¾” FNPT Recirc Return
¾” Gas
1 ½” NPT Cold Supply
¾” Combo Drain and Cold Inlet to Tankless

## Slide 33
Water connection locations help to stratify the water temperatures in the tank keeping the upper tank full of the hottest water. Provides the best energy efficient supply of hot water.
This extends the 70% rule associated with tank heaters
BASIC OPERATION

## Slide 34
TACO 009FS5 SYSTEM PUMP
(4 – 5 GPM)
All internal controls for operation are pre-plumbed and install ready
UNDER THE HOOD
Inlet Filter
Error Indicator Light
Pump Controller
Transformer
Remote Control

## Slide 35
The Hybrid Hot doesn’t come with a power cord. The contractor will need to purchase and wire
Hot
Neutral
ELECTRICAL WIRING

## Slide 36
Water Piping Diagram. Piping can be either first in, last out or in parallel
MULTIPLE PIPING
Gas Supply
Pump
Hot Water Return
Expansion Tank (Install according to local code)

## Slide 37
When common venting Hybrid Hot Water heaters, a system controller (SC-401-6M or 12M) must be installed (purchased separately).
Multi unit systems require pressure balancing of the piping system (Piping in Parallel or first in last out).
System bypass controls are set to stay open to 160ºF
COMMON VENTING

## Slide 38
Hybrid Hot install at the State of Washington Facilities complex, Whidbay Island, Washington
One of two Hybrid Hot installs at Farmer Boys Burgers, So. Cal

## Slide 39: CMK and CRK Commercial Systems
Introducing the new Noritz Complete Commercial System Bundles

## Slide 40
Easy to Transport
Sturdy Aluminum Frame
Assembly uses only 12 Bolts vs 60 Bolts of Competitor Racks!
Install in Less Than 2 Hours
True Commercial Manifold
Best Value in the Industry
Retrofit Easy Button
CMK and CRK Systems Features & Benefits
CRK-BASE + CMK-BB4 Shown, NCC199CDV Pro Units Sold Separately.

## Slide 41
CMK-SS2
Wall Hanging Side by Side Commercial Manifold Kit featuring 2 NCC199CDV Tankless Water Heaters (sold separately)
Max BTU/h: 399,800
CMK-SS3
Wall Hanging Side by Side Commercial Manifold Kit featuring 3 NCC199CDV Tankless Water Heaters (sold separately)
Max BTU/h: 599,700
Side by Side
CMK-SS4
Wall Hanging Side by Side Commercial Manifold Kit featuring 4 NCC199CDV Tankless Water Heaters (sold separately)
Max BTU/h: 799,600
CMK (Commercial Manifold Kit) System Configurations

## Slide 42
CMK-BB2
Commercial Manifold Kit connecting 2 Back to Back NCC199CDV Tankless Water Heaters (sold separately) installed on CRK Base – Floor standing rack (sold separately)
Max BTU/h: 399,800
CMK-BB4
Commercial Manifold Kit connecting 4 Back to Back NCC199CDV Tankless Water Heaters (sold separately) installed on CRK Base – Floor standing rack (sold separately)
Max BTU/h: 799,600
CMK (Commercial Manifold Kit) System Configurations
Back to Back

## Slide 43
CRK-BASE
The CRK-BASE commercial rack kit allows for custom floor standing installations of 1 to 4 tankless units.
CRK-ADDON
The CRK-ADDON commercial kit lets you expand your existing system to more than 4 units.
CRK (Commercial Rack Kit) System Configurations

## Slide 44
CMK (Commercial Manifold Kit) Additional Notes
Common Header Diameter Recommendation
One CRK-ADDON may be used per CRK-BASE. Attempting to use multiple CRK-ADDON may result in misaligned water and gas manifolds.
Up to 24 NCC199CDV Pro heaters can be connected using multiples of the CRK-BASE and CRK-ADDON kits. Quick Connect Pro up to 8 units or use a 6, 12 or 24 unit system controller (sold separately) to ensure system balancing and load management.
NCC199CDV Pro units may be common vented, refer to the common vent manual for full details.
Manifold sizing is designed for a maximum of eight (8) water heaters. In order to connect units in greater number than eight, a common header of a larger diameter may be necessary. Refer to local plumbing and/or building code for minimum pipe sizing requirements.

## Slide 46
Pre-Engineered & Pre-Fabricated
Tankless
Tankless with Storage
MULTI SYSTEM TANKLESS SOLUTIONS

## Slide 47
CR61 Commercial Rack System
VS.
TTS-S & TTS-TWST
Synergy Series
FEATURES | CR61 | TTS-S | TTS-TWST
Pre-Engineered | X | X | X
Pre-Wired System Controller | X | X | X
Water Pre-Plumbed | X | X | X
Gas Pre-Plumbed | X | X | X
Shut Off Valves / Service Valves | X | X | X
Condensate Pre-Plumbed | X | X | X
Fits Through 3’0 x 7’0 Door | X | X | X
Power OPC |  | X | X
Breaker Box with Included Circuit Breakers |  | X | X
Surge Protector |  | X | X
Building Recirculation |  | X | X
Pump Control & Timer |  | X | X
Most Compact Footprint |  | X | X
Expansion Tank |  | X | X
ECM Circulator for Storage Tank |  |  | X
System Pump Bypass |  |  | X
Storage Tank Manifolds |  |  | X
115 Gallon Storage Tank |  |  | X
Storage Tank and Building Check Valves |  |  | X
Y Strainer |  |  | X
Pre-Configured Control Wiring |  |  | X
Building Supply and Return Well Immersed Temperature Gauges |  |  | X
COMPARISON

## Slide 48
COMMERCIAL RACK SERIES (CR)
INCLUDES:
NCC199CDV PRO w/ industry leading 0.98 UEF (GQ-C3261WZ-FF-1 US)
System Controller (SC-401-6M)
Remote Control Cord (RC-CORD-10)
2” Copper Manifold for Hot & Cold
2” Black Iron Manifold for Gas
3/4” PVC Manifold Condensate Drain
Aluminum Frames
Isolation Valves w/ PRV for Water
Gas Shut Offs
Serial Number Barcode tags
Individual Heater Number Label
HOT WATER SUPPLY CAPACITY

## Slide 49
Kenny Deel Stadium – Melissa Texas ISD
4 Separate Racks – 9 total units – Main Stadium

## Slide 50
What is TTS?
The TOTAL TANKLESS SOLUTION
Why SYNERGY?
We’re Synergizing Multiple Technologies & Resources for the Best Commercial Water Heater System Available

## Slide 51
Best Warranty
In Industry
High Efficiency
98% TE 0.98 UEF
TDR 16:1 Each Tankless Engine
24 units = TDR 384:1
One Point of Connection
Water
Power
Gas
Condensate
Recirculation
Storage
Ability to combine
multiple heaters in
the smallest footprint
as well as the ability
to fit through any
3’-0” x 7’-0”
commercial door
Professionally
integrated
accessories within
the aluminum frame
Providing optional
storage water heater
integration
REDUCTION IN LABOR HOURS | FULL SOLUTION FOR CUSTOMER | WORRY-FREE INSTALLATION
Most Unmatched Complete Water Heater Solution in the Industry
Commercial Market Segments / Verticals to Target:
Education: K – 12 University Dorms
Restaurants
Assisted Living Senior Care
Multi Family

## Slide 52: S Series
The S Series comes with all the necessary equipment needed for a 2 to 6 tankless commercial system.
Features
One Point of Connection
Aluminum Frame
2 to 6 – Noritz NCC199CDV (GQ61) Tankless Water Heaters with
System Controller
1 ½” Water & Gas Manifolds
¾” Condensate Drain Manifold
Expansion Tank Included
Neutralizer Included
Breaker Box w/ Included Circuit Breakers
Pump Controller with Timer
Surge Protector
ECM Building Recirculation Pump
Shutoff Valves
Well Immersed Thermistors for Easy Monitoring of Building Hot Water
Performance

## Slide 53: SWH Series
The SWH Series provides the most complete commercial water heater solution in the market. This tankless water heating system provides up to 799,600BTU/hr. in a wall mounted platform for maximizing unutilized space, with built in redundancy and equalization of heating performance
Features
One Point of Connection
Aluminum Frame
2 to 4 – Noritz NCC199CDV (GQ61) Tankless Water Heaters with System
Controller
1 ½” Water & Gas Manifolds
¾” Condensate Drain Manifold
Expansion Tank Included
Neutralizer Included
Breaker Box w/ Included Circuit Breakers
ECM Pump Controller with Timer
Surge Protector
Building Recirculation Pump
Shutoff Valves
Well Immersed Thermistors for Easy Monitoring of Building Hot Water
Performance

## Slide 54: S Series
Power supplies each outlet
Breaker Box
Surge Protector
Temperature Probe
Flange Valve
Flange Valve w/ Service Port
5 GPM ECM Building Recirculation Pump
Junction Box
Pump Timer w/ 90 hr Battery Back Up
3/4” Building Return Line Connection
Dixell Control for Pump
PUMPS & CONTROLS

## Slide 55: S Series
Hot Water Outlet Thermometer
HOT WATER THERMOMETER

## Slide 56: S Series
PLUMBING
Isolation valve
Check Valve

## Slide 57: S Series
#1 Unit is the Main unit and where the commercial remote wires to communicate with the system controller
Labeled (System Controller) Installed
SYSTEM CONTROLLER

## Slide 58: S Series
WATER/GAS CONNECTIONS
Cold Water Isolation Valve
Gas Valve w/ Union
Hot Water Isolation Valve w/ PRV

## Slide 59: S Series
1 ½” Cold Water Manifold, End
1 ½” Gas Manifold, End
1 ½” Hot Water Manifold, End
MANIFOLDS
¾” Condensate Drain, Open

## Slide 60: S Series
EXPANSION TANK CONNECTION
Expansion Tank Thread Connection
Hose, Drain Port
Valve w/ Turn Wheel
Expansion Tank Isolation Valve

## Slide 61: S Series
2” PVC exhaust venting
2” PVC air intake venting
BOTTOM UNITS PRE-VENTED

## Slide 62: S Series
2” Gas Stand-Pipe Inlet Connection
1-1/2” Cold Water Inlet Connection
1-1/2” Hot Water Outlet Connection
Behind rack
WATER/GAS CONNECTIONS

## Slide 63: S Series
INCLUDED ACCESSORIES
Condensate Neutralizer
Literature Rack w/ Manuals & Commercial Remotes
4.4 Gallon
Expansion Tank

## Slide 64
• One Point of Connection
• Aluminum Frame
• 2 to 6 – Noritz NCC199CDV Tankless Water Heaters with System
Controller
• 115 Gallon Storage Tank Included
• 1 ½” Water & Gas Manifolds
• 2” Gas Inlet Connection
• ¾” Condensate Drain Manifold
• Expansion Tank Included
• Breaker Box w/ Included Circuit Breakers
• Pump Controller with Timer
• Surge Protector
• ECM Building Recirculation Pump
• ECM Storage Tank Recovery Circulator
• Shutoff Valves
• Well Immersed Thermistors for Easy Monitoring of Building Hot Water
Performance
• 2” Hot Water Supply to Storage Tank
• 2” Cold Make Up Water
• 2” Supply through Pump to Tankless
• 2” Pump Bypass
• Integrated 2” Check Valves
TWST Series
(Tankless w/ Storage)

## Slide 65
Differences between S Series
BUILDING PUMP & RETURN LINE
TWST Series
(Tankless w/ Storage)
1” Building Return Line Connection

## Slide 66
Additional Dixell Control for System Pump
CONTROLS
Differences between S Series
TWST Series
(Tankless w/ Storage)

## Slide 67
ECM System Pump
SYSTEM PUMP
Differences between S Series
TWST Series
(Tankless w/ Storage)

## Slide 68
2” Isolation Valve for Pump
2” Isolation Valve for Pump
2” Bypass Piping
2” Isolation Valve for Bypass
Differences between S Series
SYSTEM PUMP PIPING
TWST Series
(Tankless w/ Storage)

## Slide 69
1” Expansion Tank Connection
1” Building Return
Differences between S Series
EXPANTION TANK & RETURN CONNECTION
TWST Series
(Tankless w/ Storage)
Behind rack

## Slide 70
Differences between S Series
WATER/GAS CONNECTIONS
TWST Series
(Tankless w/ Storage)
Behind rack
2” Gas Inlet Connection
2” Return from Storage Tank Connection
2” Hot Water Outlet to Storage Tank includes Building Flow check
2” Cold Inlet Connection Includes building Back Check

## Slide 71
INCLUDED ACCESSORIES
TWST Series
(Tankless w/ Storage)
Condensate Neutralizer
Literature Rack w/ Manuals & Commercial Remotes
20 Gallon Expansion Tank

## Slide 72
Cold Water Inlet
Hot Water Outlet
S Series
Sequence of
Operations

## Slide 73
Building Return Inlet
Sequence of
Operations
S Series

## Slide 74
In a multi-system setup, the Noritz commercial units will communicate with one another and work in unison to even out the load on each individual unit, maximizing output and system life.
With the ability to modulate between multiple units with the use of a system controller makes Noritz commercial water heaters the most efficient water heating system on the market today.
INTELLIGENT SYSTEM
S Series
1 heater will work solely until the demand grows greater than 50%
50%

## Slide 75
The load will equalize among more heaters to meet high volume demand.
INTELLIGENT SYSTEM
S Series
50%
50%
50%
50%

## Slide 76
The Noritz modular system is based on a single self-contained, interchangeable unit that can combine and communicate with like units to meet any hot water demand.
No. 1 | No. 2 | No. 3 | No. 4
No. 4 | No. 1 | No. 2 | No. 3
No. 3 | No. 4 | No. 1 | No. 2
No. 2 | No. 3 | No. 4 | No. 1
Main water heater
Main water heater
Main water heater
Main water heater
Rotation
Rotation
Rotation
Rotation
MODULAR OPERATION
S Series
No. 1 | No. 2
No. 4 | No. 3

## Slide 77
If 1 unit is inoperable due to maintenance or issues, the other units can pick up the demand.
Ensuring the property NEVER loses hot water.
MODULAR OPERATION
S Series

## Slide 78
Cold Water Inlet
Hot Water Outlet
TWST Series
Sequence of Operation

## Slide 79
Storage Tank Return
System Pump Increases to Ramp Up Tankless Units to Bring Storage Tank Back to Temperature Set Point
TWST Series
Sequence of Operation
Cold Water Inlet
Hot Water Outlet

## Slide 80
Building Return Inlet
Building Recirculated Water being mixed with Inlet
TWST Series
Sequence of Operation
Cold Water Inlet
Hot Water Outlet

## Slide 81
Cold Water Inlet
Hot Water Outlet
Building Return Inlet
Dixel Temperature Controller & Sensor (Set Point at 145 F with a 3  F Dif)
145 F
160 F
160 F
160 F
160 F
160 F
160 F
155 F
Tank Temperature Settings controlled by Pump Control & System Pump
145 F
Thermistor
TWST Series
Sequence of Operation

## Slide 82
Cold Water Inlet
Hot Water Outlet
Building Return Inlet
160 F
160 F
160 F
160 F
160 F
160 F
155 F
142 F
145 F
145 F
High Demand
DUMP LOAD
System Pump Increases to Ramp Up Tankless Units to Bring Storage Tank Back to Temperature Set Point
Tank Temperature Settings controlled by Pump Control & System Pump
TWST Series
Sequence of Operation
Dixel Temperature Controller & Sensor (Set Point at 145 F with a 3  F Dif)
Thermistor

## Slide 83
Cold Water Inlet
Hot Water Outlet
Building Return Inlet
System Pump is Inoperative
Bypass – When Servicing System Pump
TWST Series
Sequence of Operation

## Slide 84
Cold Water Inlet
Hot Water Outlet
Building Return Inlet
Same Bypass Option if Storage Tank needs to be Replaced
Water Heating Completely Dependent on Tankless
TWST Series
Sequence of Operation
Bypass – When Servicing System Pump

## Slide 85
Professionally crated and available through National Distribution
SHIPPING CRATE

## Slide 86
Baltimore, MD
Before
JOHNS HOPKINS UNIVERSITY
After

## Slide 87
TTS-TWST10
Replaced 3Mbtuh input mid efficiency boiler w/ 1.9 Mbtuh 98% condensing commercial tankless technology
2 x 175G ASME Tank
ASME Expansion tank
Neutralizer
ECM System pump and controls
Building recirculation pump and controls
110:1 turn down ratio
10 year HEX warranty
5 year parts warranty
1 year reasonable labor
New Orleans, LA
COTTON MILL APARTMENTS

## Slide 88
Allen, TX
ALLEN INDEPENDENT SCHOOL DISTRICT

## Slide 89
B
FOOTPRINT DIMENSIONS
A

## Slide 90
www.noritz.com/commercial-sizing-calculator/
NORITZ ONLINE SIZING

## Slide 91
What Is A FIOP?
Factory Installed Options
If a standard offering doesn't fit the needs
Allows for the most complete solution from the factory
TTS ONLY SIZING – FRG WEBSITE

## Slide 92
WHERE TO FIND FIOP SIZING?
www.webfrg.com/tts
Get a TTS FIOP Quote

## Slide 93
Choose your application
By choosing you application you will see the options for the most common fixtures used in that application
USING FIOP FORM

## Slide 94
All Red Asterisk* Fields must be filled in. Enter “O” if not applicable
USING FIOP FORM
Multi-Family Example
Correctional Facility Example

## Slide 95
Ensures the client is getting what they need
All while maintaining our TTS Features
Professionally Crafted – Expertly installed
WHY FILL OUT A FIOP FORM?

## Slide 96
EQUIPMENT SIZING – TANKLESS ONLY

## Slide 97
Have a question on specs, sizing or how you can build Noritz into your next project? Talk to our commercial experts directly.
commercial@noritz.com
Case Studies, Resources, Technical Documents, Sizing Calculator:
www.noritz.com/commercial
Juan Rivera
Commercial Application Engineer
Jrivera@noritz.com
COMMERCIAL CONSULTATION

## Slide 98
SUPERIOR WARRANTIES

## Slide 99
THANK YOU