## Slide 1
Upgraded PRO Series

## Slide 2
OUTLINE
New Upgraded PRO Series Units
  Model Numbers
  Industry Leading Features
  New Features
  Operation Panel
    Main Menu
    Settings Menu
    Service Menu
  Bluetooth App Updates

## Slide 3
MODEL NUMBERS
Model Number
Trade Name Old New
EZ111DV GQ-C3261WX-FF US GQ-C3261WX-FF-1 US
EZ98DV GQ-C2861WX-FF US GQ-C2861WX-FF-1 US
EZ71DV GQ-C2661WX-FF US GQ-C2661WX-FF-1 US
NRCR111DV GQ-C3261WXQ-FF US GQ-C3261WXQ-FF-1 US
NRCR92DV GQ-C2661WXQ-FF US GQ-C2661WXQ-FF-1 US
NCC199CDV GQ-C3261WZ-FF US GQ-C3261WZ-FF-1 US
*Hybrid Hot and Pre-Made Rack Systems are TBD on release of new version

## Slide 4
INDUSTRY LEADING FEATURES
PRO Series units have Industry Leading Features that apply to all units
Warranty
  EZ PRO Series – 25 years on the heat exchanger
  NRCR PRO Series – 15 years on the heat exchanger
  CDV PRO Unit – 10 years on the heat exchanger
  Hybrid Hot PRO System – 10 years on the heat exchanger & tank
Energy Efficiency – 0.98 UEF on all units
Bluetooth App
Versatile Venting
  Direct Vent
  Single Vent
  Outdoor
  Flex Vent (EZ & NRCR only)
  No Roof Kit

## Slide 5
NEW UPGRADED FEATURES
Same Industry Leading Product with additional features
Built-in Operation Panel
Vacation Mode
Quick Connect Pro:
Up to 8 NCC199CDV PRO and you can monitor all 8 at the same time
Change Pump Speed on NRCR

## Slide 6
OPERATION PANEL
Operation Panel has replaced the built-in display
Waterproof keypad
All unit setting and MM information available at your fingertips

## Slide 7
Operation Panel has 6 buttons:
Back Button
OK Button
Up and Down Buttons
Menu Button
Power Button
Main Display shows:
Bluetooth Pairing Code
LP Gas Icon
Screen Lock Icon
Burner On Icon
Time
Flow Rate of System
Recirculation Icons
Set Temperature (over 120 F – Hi-Temp is displayed)
Vacation Mode Icon
Screen is illuminated Blue, but when there is a warning or error code, it illuminates Red
OPERATION PANEL

## Slide 8
MAIN MENU
Enter the Main Menu by pushing the button
1. Status
8. Maintenance Monitor
2. Recirculation
9. System Maintenance Monitor
10. Error History
Main Menu 1/3
Main Menu 2/3
Main Menu 3/3

## Slide 9
Settings Menu is for adjusting the Operation Panel Display along with setting maximum hot water temp and clock
1. Max Set Temperature
9. Screen Lock
2. Clock
SETTINGS MENU

## Slide 10
1. Maintenance Menu 1/2
3. Maintenance Writer
1. Maintenance Menu 2/2
4. Language
Only Service Menu can be changed to Spanish
1. Installer Menu 1/3
1. Installer Menu 2/3
1. Installer Menu 3/3
To enter the Service Menu, Push and Hold both Arrow Keys
SERVICE MENU

## Slide 11
EZ Start PLUS App has been updated
Installer Authentication Setting Screen
Users don’t have access to Unit Settings or Trial Operation
Vacation Mode
10 saved slots within Unit Setting Menu
BLUETOOTH APP UPDATES

## Slide 12
Best Efficiency
Best Warranty
Best Heater
Best Support
Now Easiest to Install
0.98 UEF

## Slide 13
SUPPORT.NORITZ.COM
NORITZ.COM/TECHTIPS
HELP.NORITZ.COM
TRAINING.NORITZ.COM
YOUTUBE.COM/NORITZAMERICA
Customer Care: 866-766-7489
HELPFUL LINKS

## Slide 14
THANK YOU