## Slide 2: TRAINING AGENDA
Combi Boiler
Essentials
Technology, Performance, and System Design
Customer Engagement and Value Identification
Competitive Positioning and Sales Strategy
Application Demand & Sizing Requirements

## Slide 3: COMBI BOILER ESSENTIALS
What Is a Combi Boiler?
How It Works
Market Context
System Comparisons

## Slide 4: COMBI BOILER ESSENTIALS
What Is a Combi Boiler?
A combi (combination) boiler provides:
  Space heating (radiant floors, baseboard, fan coils)
  Domestic hot water (DHW) for faucets, showers, appliances
Combines heating boiler + water heater into one compact unit
No storage tank required
Immediate value: space savings + efficiency

## Slide 5: COMBI BOILER ESSENTIALS
How Noritz Combi Boiler Works
Heating Only
Hot Water
Closed loop system
Hot water heated by primary & secondary heat exchangers
Recirculated hot water to provide space heating comfort
Heating
DHW
3-Way Valve: Variable Distribution Control

## Slide 6: COMBI BOILER ESSENTIALS
How Noritz Combi Boiler Works
Domestic Hot Water Only
3-Way Valve: Variable Distribution Control
DHW
Heating
Hot Water
Hot water to fixture demand
Heated by flat plate heat exchanger
Hot water for heating heats flat plate heat exchanger

## Slide 7: COMBI BOILER ESSENTIALS
How Noritz Combi Boiler Works
Simultaneous Heating & DHW
3-Way Valve: Variable Distribution Control
DHW
Heating
Hot Water
Our ADVANCED technology provides BOTH Heating and Domestic Hot Water simultaneously
Homeowners can use showers or faucets without shutting off or noticeably reducing home heating, ensuring consistent comfort

## Slide 8: COMBI BOILER ESSENTIALS
Market Context
Market Shift
Strong Demand
Large Storage & Low-Efficient Atmospheric Systems
High-Efficient,
Compact Solution
Retrofits
  Replacing aging boilers and storage tanks
Urban Housing
  Condos, townhomes, accessory dwelling units (ADUs)
New Construction
  Energy codes
  Smaller footprint
  Reduction in termination for furnace
Combi boilers win where space, efficiency, simplicity, & high utility rebates are primary drivers

## Slide 9: COMBI BOILER ESSENTIALS
System Comparisons
Tank Water Heater
System Boiler & Indirect Tank
Most Combi Boilers
Endless Hot Water, Higher Efficiency, No Standby Loss
Lower Upfront Cost, Smaller Footprint, Fewer Components
Best overall comfort control with simultaneous performance, most combi boilers will do heating OR domestic hot water
Noritz Combi Boiler VS

## Slide 10: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Core Technologies
Performance Metrics
System Design Fundamentals
Venting Options
Wiring Options
Plumbing Diagrams
Heating Applications

## Slide 11: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Core Technologies
Burner & Heat Exchangers
Single stage, Ceramic fiber
Significantly reduces harmful flue gases
Premix Burner
Primary Heat Exchanger
Secondary Heat Exchanger
ASME H Stamp
316L Austenite Stainless Steel, most Corrosion Resistance Material
316L Austenite Stainless Steel
Pre-heats water with exhaust gases

## Slide 12: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Core Technologies
Heat Exchanger
Flat Plate Heat Exchanger
SCR (Stress Corrosion Resistant) Austenite Stainless Steel
Indirectly heats the DHW side of the system, less scale build up on the DHW side due to the lower heating temperatures

## Slide 13: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Performance Metrics
Models (2) | NRCB180DV | NRCB199DV
Standard Gas Input (BTUH) | Min: 18,000 Max: 180,000 | Min: 18,000 Max: 199,900
Heating Gas Input (BTUH) | Min: 18,000 Max: 100,000 | Min: 18,000 Max: 120,000
DHW Flow Range (GPM) | 0.4 – 9.8 | 0.4 – 11.1
AFUE | 95% | 
DHW Burner Off Flow (GPM) | 0.29 | 
Heating Temp Range | 100F – 180F (As low as 80F with setting) | 
DHW Temp Range | 90F – 140F | 
Simultaneous Heating & DHW | YES | 
Max Elevation | 10,000 feet | 
Connection Sizes | ¾” DHW & Gas, 1” Heating, ½” Auto Feeder & Condensate | 
Quick Connect Capable | YES (With same BTU EZ or CDV Unit) | 
Outdoor Temp Sensor | INCLUDED | 
Warranty | 10 Year Heat Exchanger, 5 Year Parts, 1 Year Labor | 
Key Specifications

## Slide 14: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Performance Metrics
Expansion
For more Domestic Hot Water demand, ADD 1 EZ Model at the same Max BTUH as the Combi
Connect with QC-2,
Quick-Connect Cord.
Mount units 3”-18” apart
IMPORTANT NOTE
Solenoid Valve is needed when using a QC System with any EZ Unit
The Solenoid Valve must be Normal Closed Valve and Slow Closing to avoid water hammer
Solenoid Valve must be
¾” 120V AC - 1.5 Amp Max

## Slide 15: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
System Design Fundamentals
Quick Temperature Control & Stability

## Slide 16: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
System Design Fundamentals
Quick Temperature Control & Stability

## Slide 17: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
System Design Fundamentals
Control Panel
Heating Control Settings
User Mode – 5 Options
1. Standard (Manual Heating Settings) most common
2. Outdoor Reset Control
3. External Control (0-10 V) not common
Installer Mode – 19 Options
Maintenance Mode
Diagnostic Mode – 3 Options
Pre-Heat Timer Setting

## Slide 18: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Venting Options
2” or 3” Diameters: PVC, CPVC, or PP Material (Horizontal / Vertical Termination Options)
Direct Vent (2 Pipes: Exhausting Outdoor and Pulling Intake Outdoor Clean Air) – 2 Terminations
Concentric Vent (Pipe in a Pipe: Exhausting Outdoor and Pulling Intake Outdoor Clean Air) – 1 Termination
Single Vent (Exhausting Outdoor and Pulling Intake from Indoor Combustion Air – 1 Termination
For Single Vent:
Minimum make up air is required. More information in Installation Manual.

## Slide 19: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Wiring Options
Circuit Board
For accessories, controls, sensors, other equipment to compliment Combi Boiler system

## Slide 20: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Plumbing Diagrams
Combi Boiler as a Water Heater Only (Space Heating to be installed in the future)
Primary/Secondary Piping with Zone Valves
Primary/Secondary Piping with Zone Pumps
Air Handler Piping
Recirculation System on DHW side
Key applications for most system needs

## Slide 21: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Plumbing Diagrams
Combi Boiler as a Water Heater Only (Space Heating to be installed in the future)

## Slide 22: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Plumbing Diagrams
Primary/Secondary Piping with Zone Valves

## Slide 23: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Plumbing Diagrams
Primary/Secondary Piping with Zone Pumps

## Slide 24: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Plumbing Diagrams
Air Handler Piping

## Slide 25: TECHNOLOGY, PERFORMANCE, AND SYSTEM DESIGN
Plumbing Diagrams
Recirculation System on DHW side
The heating might not operate in some conditions during recirculation
Insulate the DHW Supply and Return pipe completely
Aquastat and timer are required to control recirc loop.
REQUIRED
This should only be installed when Heat loop is set minimum 20 F higher than the domestic side. If not possible then Quick Connect system with recirculation would be recommended.
Flow on recirculation pump should be from 1 to 1.5 gpm.
(If higher, simultaneously heating and DHW may not work)

## Slide 26: HEATING APPLICATIONS
Hydronic Systems
Warm water circulates through tubing embedded in floors.
  Best for:
    New construction
    High-efficiency homes
    Comfort-focused customers
  Key advantage
    Low-temp operation = high efficiency
Radiant Floor Heating

## Slide 27: HEATING APPLICATIONS
Hydronic Systems
Baseboard Units along walls
  Best for:
    Retrofits
    Traditional homes
  Key advantage
    Simple, proven
Baseboard Radiators (Fin-Tube)

## Slide 28: HEATING APPLICATIONS
Hydronic Systems
Integrated into limited wall spaces
  Best for:
    Modern hydronic retrofits
    Zoned comfort
  Key advantage
    Faster response than radiant
Panel Radiators

## Slide 29: HEATING APPLICATIONS
Hydronic Systems
Integrated into limited wall spaces
  Best for:
    Driveways, walkways
  Key advantage
    Activating the heating only when needed, reducing labor and time spent snow removal.
Snow Melt
NOTE
A flat-plate heat exchanger may need to be installed due to the limit of 35% glycol limit of the NRCB

## Slide 30: HEATING APPLICATIONS
Hydronic Systems
Equipment designed to regulate and circulate air within a building using hot water
  Best for:
    Gas furnace replacement
    In conjunction with cooling source
  Key advantage
    Complete system
Air Handler

## Slide 31: HEATING APPLICATIONS
Hydronic Systems
Utilizes hot water to move heated air
  Best for:
    Ceiling application
    Localized rooms
  Key advantage
    Smaller, self-contained device
Fan Coil Unit

## Slide 32: HEATING APPLICATIONS
Hydronic Systems
New Construction – Builder Advantage
  Baltimore, MD
    Single-Family Home (Tankless with Gas Furnace)
Use Case
Insulation
Insulation
3" PVC
Termination Direction
3" PVC
4 Terminations

## Slide 33: HEATING APPLICATIONS
Hydronic Systems
New Construction – Builder Advantage
  Baltimore, MD
    Townhome (Tankless with Gas Furnace)
Use Case
Insulation
Insulation
5" PVC
Concentric
2" PVC
3 Terminations
1 – Side
2 - Roof

## Slide 34: HEATING APPLICATIONS
Hydronic Systems
New Construction – Builder Advantage
  Baltimore, MD
    Multi-Family (Tankless with Gas Furnace)
Use Case
5" PVC
Concentric
4 Terminations – 2 Dwellings
2 – Side
2 - Roof
3" PVC
5" PVC
Concentric
3" PVC

## Slide 35: HEATING APPLICATIONS
Hydronic Systems
New Construction – Builder Advantage
  Installers are struggling with venting water heater and gas furnace
  Not ideal in attic and mechanical rooms
Use Case - Challenges

## Slide 36: HEATING APPLICATIONS
Hydronic Systems
New Construction – Builder Advantage
  Use Case: Cost Reduction
Heating Coil - Solution
Heating Coil placed on top of evaporator coil
Cooling Application
Heating Application
Heating Coil Not Operating
Evaporating Coil Operating
Evaporating Coil Not Operating
Heating Coil Operating
Warm Air
Return
Cold Air
Return
Cold Air
Supply
Warm Air
Supply
This option ELIMINATES
Gas Heat Exchanger as well as
Terminations for intake & exhaust

## Slide 37: HEATING APPLICATIONS
Hydronic Systems
Heating Coil - Solution
3" PVC
3" PVC
4 Terminations
2" PVC
2 Terminations
Tankless with Gas Furnace
Combi with Heating Coil
Single-Family Home

## Slide 38: HEATING APPLICATIONS
Hydronic Systems
Heating Coil - Solution
Tankless with Gas Furnace
Combi with Heating Coil
Townhome
5" PVC
Concentric
2" PVC
5" PVC
Concentric

## Slide 39: HEATING APPLICATIONS
Hydronic Systems
Heating Coil - Solution
Tankless with Gas Furnace
Combi with Heating Coil
Multi-Family
5" PVC
Concentric
3" PVC
5" PVC
Concentric
3" PVC
5" PVC
Concentric
5" PVC
Concentric

## Slide 40: HEATING APPLICATIONS
Hydronic Systems
Heating Coil
New Construction – Builder Advantage – Other Features
  40/60/80/100 KBTU heating coils available
  Direct connection between combi boiler and heating coil.
    Primary/secondary system and external/additional pump are not required.
  No electrical wiring is required to the heating coil.
    Heating is controlled by the combi boiler (and room thermostat)
  Heating coil can be put anywhere on the duct system.
    Simultaneous DHW/Heating technology.
  Less water quality issue (scale/corrosion) than regular tankless water heaters

## Slide 41: CUSTOMER ENGAGEMENT AND VALUE IDENTIFICATION
Target Customer Segments
Customer Pain Points
Translating Features → Benefits
Value Drivers by Persona

## Slide 42: TARGET CUSTOMER SEGMENTS
Homeowners
Contractors
Builders / Developers
Retrofit: replacing old boiler + tank New build: efficiency + space
Ease of install Callbacks and service friendliness
Cost per unit Mechanical room footprint

## Slide 43: CUSTOMER PAIN POINTS
Rethinking Home Comfort: Heating & Hot Water, Simplified
Today’s systems are outdated, inefficient, and frustrating. There’s a better way.
Most homes are still running two separate systems.
A boiler/furnace + a tank water heater.

## Slide 44: CUSTOMER PAIN POINTS
1
Running Out of Hot Water
2
Inconsistent Temperature
3
Rising Energy Costs
4
Space Constraints
5
System Complexity
Everyone has experienced it—back-to-back showers and suddenly… cold water.
Impact:
Household frustration Peak demand failures

## Slide 45: CUSTOMER PAIN POINTS
1
Running Out of Hot Water
2
Inconsistent Temperature
3
Rising Energy Costs
4
Space Constraints
5
System Complexity
Temperature swings during showers or
fixtures running simultaneously.
Impact:
Poor user experience Perception of unreliable system

## Slide 46: CUSTOMER PAIN POINTS
1
Running Out of Hot Water
2
Inconsistent Temperature
3
Rising Energy Costs
4
Space Constraints
5
System Complexity
Traditional systems waste energy
just keeping water hot.
Impact:
Higher monthly bills Inefficient standby losses

## Slide 47: CUSTOMER PAIN POINTS
1
Running Out of Hot Water
2
Inconsistent Temperature
3
Rising Energy Costs
4
Space Constraints
5
System Complexity
Mechanical rooms, garages, & basements
are crowded - especially in modern homes.
Impact:
Lost usable space Installation limitations

## Slide 48: CUSTOMER PAIN POINTS
1
Running Out of Hot Water
2
Inconsistent Temperature
3
Rising Energy Costs
4
Space Constraints
5
System Complexity
Two appliances = more parts,
more failure points, more confusion.
Impact:
Harder to service More things that can break

## Slide 49: CUSTOMER PAIN POINTS
The Turning Point: There Has to Be a Better Way
Bridge from frustration to solution
Homeowners don’t want more equipment
they want a smarter solutions

## Slide 50: TRANSLATING FEATURES → BENEFITS
The Turning Point: There Has to Be a Better Way
High AFUE
Lower monthly bills
Compact design
More usable space
Superior Stainless Steel heat exchangers
Longevity & reliability
Simultaneous Performance
Uninterrupted Comfort

## Slide 51: VALUE DRIVERS BY PERSONA
Homeowner
Contractor
Builder
comfort, savings, peace of mind
simple install, fewer callbacks
cost‑effective, compact, code‑friendly

## Slide 52: COMPETITIVE POSITIONING AND SALES STRATEGY
Objection Handling
Pricing & ROI Story
Sales Process Framework

## Slide 53: OBJECTION HANDLING
Not enough hot water
Too expensive
Complicated install
Maintenance concerns
Confirm sizing Explain realistic capacity Add an EZ Model
Compare total installed cost Highlight energy savings & rebates
Pre‑assembled components Contractor‑focused design
Simple annual service Long‑term reliability story

## Slide 54: PRICING & ROI STORY
Lower operating cost vs traditional systems
Reduced venting, equipment, and footprint costs
Rebates and efficiency incentives
Payback over system lifespan, not just day one

## Slide 55: SALES PROCESS FRAMEWORK
Discovery – Understand Before You Sell
Product Match – Engineer the Right Solution
Qualification – Is This a Real Opportunity?
Value Presentation – Sell Outcomes, Not Equipment
Confident Close – Guide the Decision
Identify the application
Understand current system pain points
Document system details
Identify potential barriers
Establish timeline
Evaluate application fit for a combi solution
Match features to needs
Address installation considerations
Position differentiation
Tie features directly to their pain points
Quantify benefits where possible
Pre-handle objections
Summarize alignment
Create urgency (when appropriate)
Define next steps
Each step should clearly connect to the next - no gaps, no assumptions

## Slide 56: APPLICATION DEMAND & SIZING REQUIREMENTS
Sizing Methodology
Additional Accessories

## Slide 57: SIZING METHODOLOGY
Calculate peak Domestic Hot Water demand (GPM)
Calculate heating load (BTUs)
Select unit that meets both requirements
Verify gas and venting feasibility

## Slide 58: ADDITIONAL ACCESSORIES
½” pressure reducing valve is needed on the auto feeder connection line to reduce the inlet water pressure to below 30 psi
Air Separator is required at the highest point of the heating system
Part # MK-NRCB-1
Premade to align with the heating supply and return ports. Shut off valves and ports to flush the HEX along with a drain port to bleed out air in the system

## Slide 59: HOW THE 5 SECTIONS CONNECT
Combi Boiler
Essentials
Technology, Performance, and System Design
Customer Engagement and Value Identification
Competitive Positioning and Sales Strategy
Application Demand & Sizing Requirements
What
it is
How it works
How to
sell it
How to
win
How to get it right

## Slide 60
QUESTIONS?